## Slide 1: Prelude
Arnaud Dethise
Ensuring Inter-Domain Loop-Freedom
in SDN-Enabled Networks
Marco Canini
Marco Chiesa

## Slide 2
Q
C
R
I
P
W
J
IXP
SDX
Edge Fabric
Espresso
B
N
M
A
Y
Z
IXP
IXP
SDX
SDX
“Send VoIP traffic on the red path”
BGP cares about:
IP Prefix
Local pref
AS path
Apps care about:
Bandwidth
Latency
Packet losses
BGP deflections
BGP
Notes: As you all know, the Internet is all about delivering traffic with high performance from A to B. Given the stringent requirements of traffic delivery, this requires continuous optimization.
Recently, we have seen that a programmatic approach to traffic delivery can be used to provide that optimization, as was shown by Google (Espresso) and Facebook (Edge).
We have also seen an academic attention to deploying that programmatic approach to IXPs.
Typically, routing is done with BGP. However, BGP is an old protocol that cares about things like IP prefixes, local-pref and AS paths. What apps actually care about are things like bandwidth, packet latency or packet loss.
This is why we want to create BGP deflections to optimize traffic delivery.
For example, suppose we want to connect nodes A and Z. BGP chooses the black path, which, for some reason, is suboptimal.
Fortunately, the IXPs support Software-Defined Networking, which we can use to create deflections. So we create a deflection “Send VoIP traffic on the red path”.
However, by doing this, we are creating inconsistencies between the control plane and the data plane. Normally, BGP ensures consistency to avoid forwarding loops.
What could happen if we break this consistency?
Let’s look in details at one part of the network.

## Slide 3
SDX1
SDX2
N
M
Z
B
A
B: Send VoIP traffic to A
N: Send VoIP traffic to M
BGP paths
Installed by | Match | Forward to
B | VoIP | A
N | VoIP | M
Notes: Take our five networks. Z is a popular destination that everyone want to reach.
Using BGP, M decides to use the MBZ path and A decides to use the ANZ path.
Now, suppose those nodes feel that BGP is too limited. They want to use SDN, which their IXP provides, to deflect traffic away from the default path.
B asks SDX_1 to send VoIP traffic to A (following the path A N Z). This is fine.
N asks SDX_2 to send VoIP traffic to M (following the path M B Z).
At this point, a loop is created and traffic is lost.
We know that sending VoIP traffic to M creates a loop. Can we prevent it?

## Slide 4: Solution: Compare the rules
Installed by | Match | Forward to
N | HTTP | M
N | SSH | Z
N | VoIP | M
B: “Send VoIP traffic to A”
✓
✓
✗
Unsafe because traffic is deflected to M
SDX1
SDX2
N
M
Z
B
A
When?
New deflection
BGP update to existing deflection
Notes: First idea: see if there are other rules that conflict with ours.
The rule “Send VoIP traffic to A” is unsafe if it leads to traffic being redirected to M.
Let’s look at all existing rules and compare them.
The table shows the rules installed. The first ones are safe because they don’t match the same traffic. The third one is unsafe.
This seems good, why would it not work ?
Those rules represent business information. As such, operators don’t want this solution that reveals the rules publicly. Can we keep the rules private ?

## Slide 5: Solution: Hide private information
From the literature: SIDR
Match
Forward to
“Send some traffic to A”
Detect non-existing loops
Rüdiger Birkner, Arpit Gupta, Nick Feamster, and Laurent Vanbever
"SDX-Based Flexibility or Internet Correctness?: Pick Two!”
SOSR 2017
SDX1
SDX2
N
M
Z
B
A
Installed by | Match | Forward to
B | VoIP | A
N | HTTP | M
Notes: We’re not the first one to look at this problem. It was introduced
It takes the deflections and throws away the Match part.
We only reveal that B wants to send _some_ traffic to A.
The consequence is that ifN deflects any traffic to M, B can’t deflect any traffic to A.

## Slide 6
Rüdiger Birkner, Arpit Gupta, Nick Feamster, and Laurent Vanbever
"SDX-Based Flexibility or Internet Correctness?: Pick Two!”
SOSR 2017
“Send some traffic to A”
Match
Forward to
“Send VoIP traffic to A”
Installed by | Match | Forward to
N | HTTP | M
N | SSH | Z
N | VoIP | M
✓
✓
✗
Unsafe if traffic is sent to M
Without leaking information?
From the literature: SIDR
Accurate detection
No privacy
Keep privacy
Detection with false positives
Secure computation
Accurate detection + Privacy
Prelude
Preserve privacy
100× less False Positives
Notes: On the left we have a solution that performs accurate verification, but without privacy.
On the right we have a solution that keeps privacy, but accepts false positives.
Our proposition: use Secure computation to perform verification and keep privacy.
We designed a solution named Prelude. Prelude preserves the privacy, but returns 100 times less false positives than SIDR.

## Slide 7: Outline
Analyzing the impact of BGP deflections
Distinct-Match primitive
Prelude system
Contributions
Notes: In this work, we mentioned three aspects.
The first one, analyzing the impact or BGP deflections, will not be part of this talk.
Let me now talk about the Distinct-Match primitive that we designed.

## Slide 8
HTTP | M
SSH | Z
VoIP | M
B: “Send VoIP traffic to A”
VoIP
Rules from N:
Safe
🛡️
Private
👀
Effective
💯
Fast
🏇
Other matches:
“any UDP”
“traffic from 10.0.0.1”
We will see later how this function allows us to detect loops
SDX1
SDX2
N
M
Z
B
A
Rule from B:
Output: M
Notes: What are we computing?
Our network, B wants to send VoIP traffic to A, which is translated as a rule.
What other rules does it need to compare to?
Suppose this is the list of rules B is competing with.
The first one doesn’t match, so we ignore it. The second one doesn’t match, so we ignore it.
The third one does match! However, it could also match other rules: “VoIP over UDP”, “VoIP from 10.0.0.1”.
So we will drop the “VoIP” part and only return ”M”.
This is the function that we want to implement. And we need it to be:
Safe, to avoid loops
Private
Effective, to avoid false positives
Fast, because it runs when there is a new deflection installed or a BGP update to some existing deflection.

## Slide 9
Alice
Bob
SMPC
SMPC
Honest but curious adversary
Follow the protocol
Try to learn about inputs
Secure Multi-Party Computation (SMPC)
Notes: To implement the function with the properties mentioned previously, we use Secure Multi-Party Computation.
SMPC is a cryptographic technique to securely compute a function between different parties who don’t trust each other.
Suppose that Alice and Bob each have some information and want to compute the result.
They will set up SMPC, encrypt their inputs, and send them to the SMPC machinery.
The response is computed securely and they receive the output, without learning each other’s input.
SMPC is only secure if we assume the adversary to be honest but curious. This means they follow the protocol, but still try to discover as much about our information as possible.
This model is sound in our scenario: all the agents are public and have business relations, so it is unlikely that they would risk their reputation by actively attacking to the other parties.

## Slide 10
B: “Send VoIP to A”
N: “Send VoIP to M” (installed)
Proto | Src IP | Dest IP | Type
* | * | * | VoIP
* | * | * | VoIP
No | No | No | No
Distinct?
Encode
Compare
Overlap
Distinct-Match
M
“No overlap”
Notes: I will now demonstrate how we implemented Distinct-Match.
We have B who wants to install a deflection “Send VoIP traffic to A”. It must verify if that deflection against already installed by N “Send VoIP traffic to M”.
We want to return “M” if there is an overlap, “no overlap” otherwise.
First, we encode that rule in multiple fields. Note: this is a high-level representation ; in reality, the rule are encode as a binary filter on packet headers.
We can then compare if any field is distinct. This is not the case, the rules are the same. There is an overlap.
We use that output as the control for a selector and return “M”.

## Slide 11
B: “Send VoIP to A”
N: “Send HTTP to M” (installed)
Proto | Src IP | Dest IP | Type
* | * | * | VoIP
TCP | * | * | HTTP
No | No | No | Yes
Distinct?
Encode
Compare
No overlap
Distinct-Match
M
“No overlap”
Notes: Same as before but there is an overlap.

## Slide 12: Distinct-Match implementation
In C++
SMPC with ABY framework
500 lines of code
One machine per SMPC entity (no parallelization)
Demmler, Daniel, Thomas Schneider, and Michael Zohner.
"ABY - A Framework for Efficient Mixed-Protocol Secure Two-Party Computation."
NDSS 2015
Notes: This table shows the results of a micro-benchmark of our Distinct-Match primitive.
The main factors are the number of rules you are comparing simultaneously (in white) and the RTT between the two entities (in black).
The following rows are showing the time required to setup the computation.
However, the setup time can be pre-computed offline (e.g. when there is no new rule to process), so we’ll skip it.

## Slide 13: Distinct-Match benchmarks
 | 1 | 50 | 500 | 5000
1 ms | 2.75 | 12.6 | 94.5 | 1033
 | 4.63 | 10.2 | 30.5 | 151
10 ms | 20.7 | 48.4 | 162 | 1086
 | 40.6 | 64.2 | 136 | 382
100 ms | 201 | 408 | 1237 | 6061
 | 401 | 604 | 1395 | 2638
Number of rules
Setup time [ms]
Setup time
Pre-computed (offline)
Latency
Notes: This table shows the results of a micro-benchmark of our Distinct-Match primitive.
The main factors are the number of rules you are comparing simultaneously (in white) and the RTT between the two entities (in black).
The following rows are showing the time required to setup the computation.
However, the setup time can be pre-computed offline (e.g. when there is no new rule to process), so we’ll skip it.

## Slide 14: Distinct-Match benchmarks
 | 1 | 50 | 500 | 5000
1 ms | 2.75 | 12.6 | 94.5 | 1033
 | 4.63 | 10.2 | 30.5 | 151
10 ms | 20.7 | 48.4 | 162 | 1086
 | 40.6 | 64.2 | 136 | 382
100 ms | 201 | 408 | 1237 | 6061
 | 401 | 604 | 1395 | 2638
Number of rules
Latency
Online time [ms]
Notes: Let’s look at the results for the online time, which is the factor that will decide how long it takes to process a new rule.
First, the baseline on the right represents the time if, without privacy, one party just send their input to the other.
When we preserve the privacy, with reasonable RTT between the entities, the time remains a few hundreds of milliseconds. Those are practical times, compared to the BGP convergence time, so this solution is actually practical.

## Slide 15: Outline
Analyzing the impact of BGP deflections
Distinct-Match primitive
Prelude system
Notes: We have seen how to compare the rules. Now we’ll discuss the Prelude system, and how the agents can actually discover loops using Distinct-Match.

## Slide 16
Installed by | Match | Forward to | Path
N | VoIP | M | M B Z
B | VoIP | A | A N Z
B → SDX1
“Deflect VoIP traffic to A
Using BGP route (A N Z)”
SDX1 checks (A N Z)
SDX2 in Path
SDX1
SDX2
N
M
Z
B
A
Notes: Let’s bring back our example from earlier.
We have two routes to Z, (A N Z) and (M B Z). N has a deflection for sending VoIP traffic to M.
B wants to install a new rule to deflect VoIP traffic to A.
First, B makes a request to SDX_1 to install the new route, along with the path it wants to use.
SDX_1 checks the path and realize the SDX_2 is on it, so there might be a deflection!

## Slide 17
SDX1 → SDX2:
Distinct-Match( enc(<r>), B → N )
Installed by | Match | Forward to | Path
N | VoIP | M | M B Z
B | VoIP | A | A N Z
SDX1
SDX2
N
M
Z
B
A
SMPC
Notes: SDX_1 takes the route request from B and will encrypt it. It then contacts SDX_2, and asks to start a Distinct-Match verification between the encrypted rule, on behalf of B, to member N.
Once SDX_2 receives the request, it will perform the SMPC verification between the new rule and the rules installed by N.
The results will depends on what deflections N has installed.

## Slide 18
Installed by | Match | Forward to | Path
N | VoIP | M | M B Z
B | VoIP | A | A N Z
Distinct-Match( enc(<r>), B → N )
Overlap? Yes
SMPC output: M
SDX2 routing table: M B Z
Rule installation refused by SDX1
SDX1
SDX2
N
M
Z
B
A
Notes: First, suppose N installed a rule that will redirect VoIP traffic to M.
The SMPC returns M. SDX_2 consults its forwarding table and learns that the path used is M B Z. B is present, so if it installs a deflection, a loop will be created.
The rule is refused.

## Slide 19
Distinct-Match( enc(<r>), B → N )
Overlap? No
SMPC output: “No overlap”
Rule installation allowed by SDX1
SDX1
SDX2
N
M
Z
B
A
Installed by | Match | Forward to | Path
N | HTTP | M | M B Z
B | VoIP | A | A N Z
With two SDXes,
Prelude detects a forwarding loop
iff it exists
Notes: Now, suppose that instead, the deflection from N deflects only HTTP traffic.
Then, when SDX_1 and SDX_2 run SMPC, the returned value is “No overlap”. Thus, the rule is safe and can be installed.

## Slide 20
Installed by | Match | Forward to | Path
N | VoIP | M | M Q Z
B | VoIP | A | A N Z
SDX3
R
Distinct-Match( enc(<r>), B → N )
Overlap? Yes
SMPC output: M
SDX2 routing table: M Q Z
SDX1
SDX2
N
M
Z
B
A
Q
Notes: Now, assume that the rule is VoIP again. There is an overlap, SDX_2 learns that there is a deflection to M, and that the route is M Q Z.
SDX_2 checks the route (MQZ), and learns that there is another SDX on the path: SDX_3.

## Slide 21
Distinct-Match( enc(<r>), B → N )
Overlap? Yes
SMPC output: M
SDX2 routing table: M Q Z
SDX1 verify
with SDX3
SDX1
SDX2
N
M
Z
B
A
SDX3
R
Q
Installed by | Match | Forward to | Path
N | VoIP | M | M Q Z
B | VoIP | A | A N Z
Notes: There are several possible scenarios with SDX_3.
First, SDX_3 could follow the announced route and reach the destination. In that case, the deflection is safe, doesn’t create a loop, and the installation is allowed.
However, it is possible that there is another deflection at SDX_3. Suppose that Q deflects VoIP traffic to R, which then sends that traffic to B. In this case, installing the deflection would create a loop.
To know which scenario is true, SDX_1 must redo the verification with SDX_3.

## Slide 22: Prelude evaluation
No False Negatives (safe)
How many False Positives?
False Positives [%]
Evaluation setup:
421 SDXes
Max 200 deflections / member
TCP/UDP + random src/dst port
28% → 0.3% False positives
28%
0.3%
8%
Notes: Now let’s evaluate how good Prelude is at detecting loops.
First, we should mention that there are no false negatives. Our goal is to ensure safety first and foremost, and avoid loops.
Thus, we evaluated the solution for false positives. We have a setup with 421 IXPs (all considered to be SDXes), each member installs up to 200 policies, and the policies are based on a random selection of port and protocol.
We compare our solution with SIDR and a solution that assumes perfect knowledge of all rules (that is, no privacy at all).
We see that when we check up to 13 SDXes in the path, the solution with perfect knowledge achieves perfect accuracy (as no valid path is over 13 hops long). Using Prelude, we managed to reduce the error rate of 28% in SIDR to just 0.3%.
However, the drawback is that we have to perform Distinct-Match at each hop. Using Distinct-Match 13 times is very costly. So, we looked at what happens when we reduce the maximal number of SDXes to explore to 6.
As we can see, there are some false positives in the solution with perfect knowledge, because some valid paths are longer than 6 hops. Most importantly, the error rate of Prelude increases to 8%, because there are valid paths that are not detected as being valid with only 6 hops (we needed more to actually detect them as valid).
Choosing the actual value of the path threshold is left to the network operator.

## Slide 23: Summary
💯 VS. 👀
Distinct-Match
Prelude
✓ ✗
Thank you!
Distinct-Match
M
“No overlap”
deflections
SDX1
SDX2
N
M
Z
B
A
28%
0.3%
8%
Notes: To conclude, we explained the problem of loops that can be created when we deflect traffic from the default BGP path with SDN.
We also mentioned that loop avoidance generally requires a trade-off between accuracy and privacy, as keeping information private leads to false positives.
We then showed the Distinct-Match primitive that allows us to get a solution that causes few false positives while preserving the full privacy of the rules in practical time.
Finally, we explained how Prelude allows us to detect whether a new rule is safe to install or would create a loop, and we compared its rejection rate of valid loops to another state-of-the-art solution and showed that our approach is significantly more accurate.

## Slide 24: Backup slides

## Slide 25: Distinct-Match benchmarks
 | 1 | 50 | 500 | 5000 | Baseline
1 ms | 2.75 | 12.6 | 94.5 | 1033 | -
 | 4.63 | 10.2 | 30.5 | 151 | 2
10 ms | 20.7 | 48.4 | 162 | 1086 | -
 | 40.6 | 64.2 | 136 | 382 | 20
100 ms | 201 | 408 | 1237 | 6061 | -
 | 401 | 604 | 1395 | 2638 | 200
Number of rules
Latency
Setup + Online time [ms]
Notes: Let’s look at the results for the online time, which is the factor that will decide how long it takes to process a new rule.
First, the baseline on the right represents the time if, without privacy, one party just send their input to the other.
When we preserve the privacy, with reasonable RTT between the entities, the time remains a few hundreds of milliseconds. Those are practical times, compared to the BGP convergence time, so this solution is actually practical.

## Slide 26: Distinct-Match Circuits (1)
R1 11x001xxx100x10…
R2 1000111xxx01110…
1 1 1 …
0 00 000000 000

## Slide 27: Distinct-Match Circuits (2)
1 1 1 …
0 00 000000 000
1
(0 if rules overlap)

## Slide 28: Distinct-Match Circuits (3)
If R1 overlaps R2
return the path
Else
return null
path
null
overlap

## Slide 29: Distinct-Match Circuits (4)
Suppose I want to know R and must follow the protocol
0xxxxx…
1xxxxx…
Output 0xxx… | Output 1xxx… | First bit of R
M | M | x
M | No overlap | 0
No overlap | M | 1
Hidden by shuffling the output (using a secret key and multiple MUX gates)

## Slide 30: SMPC Protocol performance (1)
delay: 50 ms
length: 13 B

## Slide 31: SMPC Protocol performance (2)
# rules: 2000
length: 13 B

## Slide 32: Number of SDXes in deflected paths

## Slide 33: Distinct-Match returned value
Q
C
R
I
P
W
J
SDX3
B
N
M
A
Y
Z
SDX2
SDX1
N @ SDX2
P @ SDX3
Z

## Slide 34: False Positives
SSH
HTTP
New rule

## Slide 35: Theorem
If the BGP policies and deflections satisfy the Gao-Rexford conditions, then the forwarding state is loop-free.
https://arxiv.org/abs/1806.09566

## Slide 36: Theorem
﻿Prelude detects a forwarding loop between two ASes at two SDXes if and only if a forwarding loop between the two ASes exists.
Moreover, the members' SDN policies are not revealed neither among SDXes or any unintended member.
https://arxiv.org/abs/1806.09566