## Slide 1: Toward Effective and Fair RDMA Resource Sharing
Haonan Qiu, Xiaoliang Wang, Tiancheng Jin, Zhuzhong Qian, Baoliu Ye, Bin Tang, Wenzhong Li, Sanglu Lu
National Key Laboratory for Novel Software Technology, Nanjing University
APNet 2018, August 2

## Slide 2: RDMA in Datacenter
RDMA NIC(RNIC)
Datacenter
Cheaper price
Low latency(~ 1us)
High throughput(100GbE)
Large scale
7 x 24h online real time service
High volume traffic (TB level)

## Slide 3: RDMA-Based Datacenter Applications
KVStore
Pilaf
[ATC’ 13]
HERD
[SIGCOMM’14]
RPC
FaSST
[OSDI’ 16]
RFP
[EuroSys’ 17]
DSM
FaRM
[NSDI’ 14]
INFINISWAP
[NSDI’ 17]

## Slide 4: RDMA Communication and Resources
Application
Kernel
RNIC
Application
Kernel
RNIC
Buf
Buf
QP
QP
CQ
CQ
Post Send WQE
Post Recv WQE
Poll CQE
Poll CQE
②
①
③ Transmission
⑤
④
WQE: Work Queue Element
QP: Queue Pair
CQ: Completion Queue
CQE: Completion Queue Element

## Slide 5: QoS of RDMA NIC
Application-level Strategy
  QPs can be mapped to different Traffic Class (TCs).
Available Mechanism for TCs
  Strict Priority (Strict)
    Prior over non strict priority TCs (ETS).
  Enhanced Transmission Selection (ETS)
    Share the left bandwidth according to a minimal guarantee policy.

## Slide 6: Explosive Volume of Resources
Cache miss will frequently happen in large-scale data center network.
RNIC
Memory
qp_context
Virt-to-phy addr
WQE
Swapping
qp_context
Virt-to-phy addr
WQE
(1) Large-scale Datacenter with large number of connections
(2) Cache miss caused by overfull meta data

## Slide 7: Resource Sharing Problem
Thread 1
Thread 2
Thread 3
QP
Lock
Lock mechanism must be applied in synchronous sharing.
The SRQs provided by verbs are application isolated and not effectively shared.
Serious performance loss when applying lock mechanism.
  34% performance loss for 6 threads
  44% performance loss for 9 threads.
(1) Synchronous Resource Sharing Model
(2) Throughput on the Shared QP with Varied number of Threads
SRQ
CQ
Resources should be effectively shared among applications

## Slide 8: QoS Demand
  Occasion
    Flows in datacenter with deadlines should be served as high priority.
    Most flows in datacenter are short flows(<50KB) and should be served quickly.
  Demand
    Short flows should not be blocked by long flows.
    The high priority flows should not be blocked by low priority flows.

## Slide 9: HoL Blocking and Corase-grained Scheduling
TC
TC
TC0(ETS)
TC1(Strict)
Processing
Processing
Processing
HoL Blocking
Corase-grained
Scheduling
Flow A
Flow B
(1) Small Flow Completion Time
(2) Small Flow Completion Time
(3) High Priority Flow Completion Time

## Slide 10: When Resource Sharing Meets QoS Demand
Application Engineers
RNIC Driver Engineers
Low-level engineers must guarantee effective QoS for our applications.
We focus on the design of base function and hardware performance of RNIC now.
Applications
Help!
All problems in computer science can be solved by another level of indirection.
Preserve the performance while adding an extra layer

## Slide 11: Goals and Model
Design Goals
  Effective resource sharing
  Fair fine-grained scheduling
Model (Avatar)
  Connection establishment
    Connections to the same remote node share the same resources (QP and Worker)
  Traffic scheduling
    Workers process WQEs from connections
  Traffic receiving
    One SRQ handels all remote QPs.
    Poller polls the CQ to distribute the traffic.
System Model

## Slide 12: Asynchronous Resource Sharing
Application
Connection
Worker
Application
Connection
fd
fd
ID:1
ID:2
S
S
Fd Vector
①
①
②
②
③
③
④
④
QP
Data structure in each connection for asynchronous resource sharing
  An unique identifier to differentiate traffic sharing the same QP.
  An egress queue to cache WQEs of each applications.
  An event file descriptor to request Avatar for service.

## Slide 13: Fair Traffic Scheduling
Fairness in the same priority
  Split traffic into same small size.
  En-queue the traffic in Round-Robin.
Fairness between High Priority and Low priority
  Split traffic into same small size.
  Traffic with low priority will not block traffic with high priority.
Connections
Low Priority
High Priority
TC(ETS)
TC(Strict)

## Slide 14: Traffic Receiving and Thread Working Mode
Traffic Receiving
  Poller polls CQ and pushes CQEs to the ingress queue of the connection according to the ID in CQEs.
Thread Working Mode
  Blocked, Interrupted, Running
    Save CPU resources in light load.
    Keep running in heavy load environment for avoiding extra latency.
Application
Connection
Poller
Application
Connection
fd
fd
ID:1
ID:2
R
R
ID Vector
①
②
SRQ
CQ
③
④
⑤
⑥

## Slide 15: Testbed Setting
Four Nodes
  CPU
    Xeon E5-2650v2(24 cores, 2.1Ghz)
  DRAM
    4 * 16GB DDR3 DIMMs, 1.6Ghz
  RNIC:
    Mellanox EDR ConnectX5 100GbE
    Mellanox QDR ConnectX3 40GbE.
  Switch
    Mellanox MSN 2100 100GbE
RoCE Node
Dell R720
NIC
Switch
RoCE Node
Dell R720
NIC
RoCE Node
Dell R720
NIC
RoCE Node
Dell R720
NIC

## Slide 16: Scalability
Scalability
  Support 1024 connections with below 20% performance loss between two nodes.
  No loss caused by mutex-lock contention among applications.
  10% - 20% higher throughput than native RDMA when connection size varies in four nodes.
  8% - 25% higher throughput than native RDMA when cluster size varies.
Connection Scalability
between 2 nodes
(2) Application Scalability
(emulated by thread) on 1 QP
(3) Connection Scalability
between 4 nodes
(4) Cluster Scalability

## Slide 17: Fairness
Fairness
  Mitigate the HoL blocking when both large flows and small flows with same priority (w/o PRI) exist.
  Achieve fine-grained preemptive scheduling when large flows and small flows with different priorities (w/ PRI) exist.
  Reducing FCT of mice flows and flows with high priority up to 50% when multiple flows exist.
(1) Round-Robin w/o PRI
(3) 8 Traffics w/o PRI
(2) Round-Robin w/ PRI
(4) 8 Traffics w/ PRI

## Slide 18: Latency and CPU Cost
Latency
  Transfer M KB data
  Extra 1~2us when M < 16 KB.
  37% less latency when M = 256KB.
CPU Cost
  Transfer 1GB, 10GB and 100GB data.
  Less time than busy-polling RDMA.
  Less Real time but more User space time than event-triggered RDMA .
(1) Latency Comparison
(2) Real Time
(3) User space Time
(4) User space + Kernel space Time

## Slide 19: Summary
Avatar
  A new model to better take advantage of RDMA
    Effective resource sharing
    Fair traffic scheduling on RNICs
    Low latency and low CPU cost

## Slide 20
Thank you!
Q&A