## Slide 1
Pas de deux: Shape the Circuits, and Shape the Apps too!
  --- Application-aware network scheduling over optical datacenter networks
Hong Zhang Kai Chen, Mosharaf Chowdhury

## Slide 2: Optical Networking in Data Centers
Advantages of optical networking
  High one-to-one bandwidth
  Low power consumption
  Low wiring complexity
  …
Extra constraints for scheduling network traffic
  Limited number of concurrent connections for each src/dst rack
  Switching/reconfiguration delay (up to 10s of ms)
Optical Fabrics

## Slide 3: What is this paper about?
Optical architecture design
  A continuing research effort towards novel reconfigurable optical datacenter designs with lower cost, better scalability, …
2016
2017
2010
  Network scheduling over the optical architecture
    How will the extra constraints of the optical fabric affect the end-to-end application performance (e.g., Spark, Hadoop applications)?
    Will the evolving optical architecture make a difference?
C-Through
2012
2013
Helios
OSA
Mordia
ReacToR
ProjecToR
MegaSwitch
How to perform network scheduling for these data-parallel applications over the state-of-the-art optical architectures?
---- Three New Challenges

## Slide 4: Challenge 1: Application Semantics
The traffic demand matrix
Dst
 | 1 | … | n
1 | - | … | *
… | … | - | …
n | * | … | -
Src
Map Stage
Shuffle
Reduce Stage
Coflow:
A collection of parallel flows sharing a common application-level goal
Completion time of a coflow depends on the last flow to complete
Minimizing coflow completion time effectively minimizes job completion time
Existing performance goal:
Maximizing the throughput or minimizing the makespan of a given traffic demand matrix
Do not directly benefit any application-level communication performance

## Slide 5: Challenge 1: Application Semantics
The traffic demand matrix
Dst
 | 1 | … | n
1 | - | … | *
… | … | - | …
n | * | … | -
Src
 | 1 | … | n
1 | - | … | *
… | … | - | …
n | * | … | -
 | 1 | … | n
1 | - | … | *
… | … | - | …
n | * | … | -
 | 1 | … | n
1 | - | … | *
… | … | - | …
n | * | … | -
App 1
App 2
App 3
Coflow 1
Coflow 2
  Coflow 3
Challenge 1: How to minimize the average completion time of all the coflows?

## Slide 6: Challenge 2: Traffic Pattern
 | 1 | 2 | 3
1 | - | … | *
2 | … | - | …
3 | * | … | -
Src
Dst
 | 1 | 2 | 3
1 | - | … | *
2 | … | - | …
3 | * | … | -
 | 1 | 2 | 3
1 | - | … | *
2 | … | - | …
3 | * | … | -
 | 1 | 2 | 3
1 | - | … | *
2 | … | - | …
3 | * | … | -
Wavelength/Circuit
assignments
1
2
3
1
2
3
1
2
3
1
2
3
1
2
3
1
2
3
Schedule 1
Schedule 2
Schedule 3
time
Switching latency
BvN decomp.
The sparse traffic demand matrix

## Slide 7: Challenge 2: Traffic Pattern
 | 1 | … | n
1 | - | … | *
… | … | - | …
n | * | … | -
Coflow i
All-to-all communication pattern
Wide-spread demand matrix
(ProjecToR, SIGCOMM’16)
time
Frequent reconfiguration
Longer coflow completion time
Challenge 2: How to efficiently deal with the wide-spread communication pattern?

## Slide 8
Circuit configuration
Constraint:
Each src/dst rack(node) can only establish one circuit concurrently.
Each connection carries a fixed capacity.
Circuit Switching
1
2
3
1
2
3
Challenge 3: Connectivity

## Slide 9: Challenge 3: Connectivity
Challenge 3: How to effectively leverage such rich connectivity of the latest optical architectures?
Circuit configuration
Packet Switching
1
2
3
1
2
3
Circuit configuration
Model/Constraint:
Each src/dst rack can establish one k circuit connection concurrently.
Each connection carries a fixed capacity.
Richer Connectivity
2016
2017
2010
C-Through
2012
2013
Helios
OSA
Mordia
ReacToR
ProjecToR
MegaSwitch

## Slide 10: The Single Coflow Case
How to effectively leverage the rich connectivity of the latest optical architectures, so that we can schedule a coflow with wide-spread communication pattern in an efficiently way?
With such rich connectivity, can we achieve optimal coflow completion time (CCT) without reconfiguring the circuit for multiple times?
Assumption: one coflow only stick to one circuit configuration, no reconfiguration during scheduling.

## Slide 11: What can be achieved via packet switching?
A
B
C
D
E
10MB
20MB
20MB
150MB
 | A-D | E
A | 0 | 10
B | 0 | 20
C | 0 | 20
D | 0 | 150
E | 0 | 0
A
B
C
D
E
0.2GBps
0.4GBps
3GBps
The Coflow demand matrix C
The rate allocation with packet switching
 | A-D | E
A | 0 | 0.2
B | 0 | 0.4
C | 0 | 0.4
D | 0 | 3
E | 0 | 0
Good Match
Can we achieve similar coflow completion time via circuit switching?
Coflow completion time: 50ms
0.4GBps

## Slide 12: Solution 1- Circuit Shaping
 | A | B | C | D | E
A | 0 | 1 | 1 | 1 | 1
B | 1 | 0 | 1 | 1 | 1
C | 1 | 1 | 0 | 1 | 1
D | 1 | 1 | 1 | 0 | 1
E | 1 | 1 | 1 | 1 | 0
Given a coflow demand matrix C, find a circuit configuration M* that minimizes the coflow completion time (CCT).
The Coflow demand matrix C
The circuit configuration M* calculated for C
1
A
B
C
D
E
1 (circuit connection)
1
1
A
B
C
D
E
10MB
20MB
20MB
150MB
 | A-D | E
A | 0 | 10
B | 0 | 20
C | 0 | 20
D | 0 | 150
E | 0 | 0
Circuit configurations
(k = 4)
{M}
Circuit Shaping
Mismatch

## Slide 13: Solution 1- Circuit Shaping
 | A | B | C | D | E
A | 0 | 1 | 1 | 1 | 1
B | 1 | 0 | 1 | 1 | 1
C | 1 | 1 | 0 | 1 | 1
D | 1 | 1 | 1 | 0 | 1
E | 1 | 1 | 1 | 1 | 0
Given a coflow demand matrix C, find a circuit configuration M* that minimizes the coflow completion time (CCT).
The Coflow demand matrix C
The circuit configuration M* calculated for C
Integrality gap
App-Topo Structure Mismatch:
The 0-1 constraint of wavelength assignment causes the integrality gap
Coflow completion time: 150ms
1
A
B
C
D
E
1 (circuit connection)
1
1
A
B
C
D
E
10MB
20MB
20MB
150MB
 | A-D | E
A | 0 | 10
B | 0 | 20
C | 0 | 20
D | 0 | 150
E | 0 | 0
Under provisioning
Under provisioning
Circuit configurations
(k = 4)
{M}
Mismatch
Circuit Shaping

## Slide 14: To Bridge the App-Topo Structure Mismatch
The Coflow demand matrix C
 | A | B | C | D | E
A | 0 | * | * | * | *
B | * | 0 | * | * | *
C | * | * | 0 | * | *
D | * | * | * | 0 | *
E | * | * | * | * | 0
Circuit configurations {M}
Cannot always find a good match
Intuition
Instead of shaping the circuit to match the coflow, can we find a way to shape the coflow demand to match the circuit configuration?
How about the reverse direction?
Circuit Shaping
 | A | B | C | D | E
A | 0 | * | * | * | *
B | * | 0 | * | * | *
C | * | * | 0 | * | *
D | * | * | * | 0 | *
E | * | * | * | * | 0

## Slide 15
A
B
C
D
E
10MB
20MB
20MB
150MB
 | A-D | E
A | 0 | 10
B | 0 | 20
C | 0 | 20
D | 0 | 150
E | 0 | 0
The Coflow demand matrix C
 | A | B | C | D | E
A | 0 | 1 | 1 | 1 | 1
B | 1 | 0 | 1 | 1 | 1
C | 1 | 1 | 0 | 1 | 1
D | 1 | 1 | 1 | 0 | 1
E | 1 | 1 | 1 | 1 | 0
A given circuit configuration M
A
B
C
D
E
150MB
20MB
20MB
10MB
Given a coflow demand matrix C and a circuit configuration M, determine a new coflow demand matrix C* which can be reshaped from the original matrix C by multihop routing, so that the coflow completion time is minimized.
Reshape
-100MB
40MB
30MB
30MB
+ 40MB
+30MB
+30MB
 | A | B | C | D | E
A | 0 | 0 | 0 | 0 | 10 + 40
B | 0 | 0 | 0 | 0 | 20 + 30
C | 0 | 0 | 0 | 0 | 20 + 30
D | 40 | 30 | 30 | 0 | 50
E | 0 | 0 | 0 | 0 | 0
The reshaped demand matrix C*
Good
Match
Coflow completion time: 50ms
Solution II - Coflow Shaping

## Slide 16
 | A | B | C | D | E
A | 0 | 0 | 0 | 0 | 10 + 40
B | 0 | 0 | 0 | 0 | 20 + 30
C | 0 | 0 | 0 | 0 | 20 + 30
D | 40 | 30 | 30 | 0 | 50
E | 0 | 0 | 0 | 0 | 0
Does coflow shaping totally solve the App-Topo structure mismatch problem?
Given an arbitrary configuration, it is not always possible to approach the optimal CCT via coflow reshaping.
Multi-hop routing may also result in an inefficient use of the circuit.
20 + 30MB
10 + 40 MB
20 + 30MB
30MB
40MB
30MB
Total Coflow demand:
200MB
Traffic introduced:
100MB + 100MB*2 =300MB
A
B
C
D
E
50MB
20 + 30MB
10 + 40 MB
20 + 30MB
30MB
40MB
30MB
Low “bandwidth efficiency”
Problem with Coflow Shaping
The reshaped demand matrix C*

## Slide 17: To Bridge the App-Topo Structure Mismatch
The Coflow demand matrix C
Cannot always find a good match
Intuition
How about we jointly shaping both circuit configuration and coflow traffic demand?
Not efficient enough as well
Circuit Shaping
Coflow Shaping
 | A | B | C | D | E
A | 0 | * | * | * | *
B | * | 0 | * | * | *
C | * | * | 0 | * | *
D | * | * | * | 0 | *
E | * | * | * | * | 0
 | A | B | C | D | E
A | 0 | * | * | * | *
B | * | 0 | * | * | *
C | * | * | 0 | * | *
D | * | * | * | 0 | *
E | * | * | * | * | 0
Circuit configurations {M}

## Slide 18: Solution III - Joint Shaping
 | A-D | E
A | 0 | 10
B | 0 | 20
C | 0 | 20
D | 0 | 150
E | 0 | 0
The Coflow demand matrix C
Circuit configurations
{M}
Circuit Shaping
 | A | B | C-D | E
A | 0 | 1 | 0 | 0
B | 0 | 0 | 0 | 1
C | 0 | 1 | 0 | 0
D | 0 | 0 | 0 | 3
E | 0 | 0 | 0 | 0
The circuit configuration M* for C*
10MB
20MB
20MB
150MB
A
B
C
D
E
 | A | B | C-D | D
A | 0 | 10 | 0 | 0
B | 0 | 0 | 0 | 20+10+20
C | 0 | 20 | 0 | 0
D | 0 | 0 | 0 | 150
E | 0 | 0 | 0 | 0
The reshaped demand matrix C*
Coflow
shaping
A
B
C
D
E
3
1
1(circuit connection)
Good match!
Coflow completion time: 50ms
Extra traffic introduced:30MB
Minimal Bandwidth Usage
Optimal Coflow completion time
Given a coflow demand C, determine the reshaped coflow demand C* and the circuit configuration M*, so that the CCT is minimized with minimal bandwidth usage.

## Slide 19: Preliminary Evaluation
Workload
  1-hour Mapreduce trace
  3000-node, 150-ToR Facebook cluster
  500 coflows (7x105 flows)
Settings
  k (available ports per ToR)= 192
  1Gbps per circuit
  Evaluate each coflow separately
Joint shaping is within 1.18× to optimal;
Joint shaping outperforms circuit shaping by 30%.

## Slide 20: The General Case with Multiple Coflows
 | 1 | … | n
1 | - | 1 | …
… | … | - | 1
n | 2 | 1 | -
 | 1 | … | n
1 | - | 1 | …
… | … | - | 1
n | 2 | 1 | -
 | 1 | … | n
1 | - | 1 | …
… | … | - | 1
n | 2 | 1 | -
Coflow 1
Coflow 2
  Coflow 3
Circuit configuration 1
Circuit configuration 2
time
…
Coflow Shape 1
Shape 2
Shape 3
Shape 4
Shape 5
An efficient scheduling decision
Goal: minimizing average CCT
Problem Definition
Hardness of the problem
A joint Optimization problem with:
  Coflow prioritization rate allocation (Strongly NP-hard)
  Circuit configuration
  Routing (Coflow Shaping)

## Slide 21: The General Case with Multiple Coflows
How to perform efficient scheduling with reasonable complexity?
------ Key: find a good way to decouple the problem.
The Inter-Coflow Scheduling Framework
High-level idea: break the problem into three steps, and each can be transformed to the single coflow problems above.

## Slide 22: The General Case with Multiple Coflows
Step 2: Coflow Prioritization
Coflow Shaping
Determine the prioritization among coflows
How to perform efficient scheduling with reasonable complexity?
------ Key: find a good way to decouple the problem.
The Inter-Coflow Scheduling Framework
Step 1: Circuit Configuration
Find a good circuit configuration for the current time slot
Joint Shaping
Determine the rate
and routing schedule
for each coflow
Step 3: Rate/routing allocation
Coflow Shaping

## Slide 23
Application-aware network scheduling over the latest optical DC architecture is an important and challenging problem which has previously received little attention.
Unveil the power of joint shaping: efficient scheduling should be a “Pas de deux” – a joint shaping of not only the underlying circuit, but also the application’s traffic demand.
A scheduling framework: an efficient decoupling of circuit configuration, coflow prioritization, and routing/rate allocation.
Takeaways

## Slide 24
Thank You!